UNO as UPDI programmer

NVM/UPDI commands

UART_Tx (download_SIB)	Data sheet 30.3.3.8
Download_SIB is defined as E5
E5 is a key instruction download 128 bytes of SIB data

In subroutine	Erase_code()

send_key(Key_chip_erase);	Initiates a device erase command

UART_Tx(LCDS | ASI_KEY_STATUS_reg);
Downloads the UPDI key status register
If bit 3 is 1 the chip erase command was successful
UPDI reset
UART_Tx(STCS | ASI_Reset_Request_reg);
UART_Tx(Reset_signature);
Sends the reset signature 0x59 to the UPDI register
Sending zero releases the rest

UART_Tx(LCDS | ASI_SYS_STATUS_reg);
Downloads the UPDI key status register
If bit zero is 0 the device is unlocked

In subroutine	set_up_NVM_prog()

send_key(Key_NVM_prog);	Initiates NVM programming

UART_Tx(LCDS | ASI_KEY_STATUS_reg);
Downloads the UPDI key status register
If bit 4 is one NVM programming key is active

UART_Tx(LCDS | ASI_SYS_STATUS_reg);
Downloads the UPDI system status register
If bit 3 is one NVM programming can start

In subroutine read_out_signature_bytes()

UART_Tx(LDS_from | word_address);
Downloads data
Must be followed by address of data

Programming flash using isolated STS commands

UART_Tx(STS | word_address);
Followed by address
Then waits for AK byte
Then sends data byte

Subroutine Write_page_to_NVM()

UART_Tx(STS | int_data);	Store integer data command
UART_Tx(NVMCTRL_ADDR_reg);	Followed by destination address
UART_Tx(NVMCTRL_ADDR_reg >> 8);	Low and high bytes
Receive Ack Pulse
UART_Tx(PA);	Page address low and high
UART_Tx(PA >> 8);	bytes to be stored
Receive Ack pulse

UART_Tx(STS | byte_data);	Store data byte command
UART_Tx(NVMCTRL_CTRLA);	Followed by destination
UART_Tx(NVMCTRL_CTRLA >> 8);	address. High & low bytes
Receive Ack pulse
UART_Tx(WP_cmd);	Send write page command
 Receive Ack pulse

Subroutine write_fuse()
For this subroutine it was found that UART_Tx(STS | int_data) would not work properly. It onlr save the lower 8 bits.
UART_Tx(STS | int_data) was therefore replace by:
UART_Tx(STS | byte_data)
UART_Tx(STS | byte_data)
as follows:

UART_Tx(STS | byte_data);	Store data byte command
UART_Tx(NVMCTRL_ADDR_reg);	Followed by destination address
UART_Tx(NVMCTRL_ADDR_reg >> 8);
Receive Ack pulse
UART_Tx(fuse_add);	Address of fuse low byte
Receive Ack pulse

UART_Tx(STS | byte_data);	Store data byte command
UART_Tx(NVMCTRL_ADDR_reg);	Followed by destination address
UART_Tx(NVMCTRL_ADDR_reg >> 8);
Receive Ack pulse
UART_Tx(fuse_add >> 8);	Address of fuse high byte
Receive Ack pulse

UART_Tx(STS | byte_data);	Store data byte command
UART_Tx(NVMCTRL_DATA_reg);	Follow by address
UART_Tx(NVMCTRL_DATA_reg >> 8);
Receive Ack pulse
UART_Tx(value);	New fuse setting
Receive Ack pulse

UART_Tx(STS | byte_data);
UART_Tx(NVMCTRL_CTRLA);
UART_Tx(NVMCTRL_CTRLA >> 8);
Receive Ack pulse
UART_Tx(cmd_update_fuse);	Send the command to update the fuse
Receive Ack pulse
Block data write to flash	(using repeat command)

UART_Tx(0x55);	//Setup word pointer
UART_Tx(ST | word_pointer);
UART_Tx(add_in_flash);
UART_Tx(add_in_flash >> 8);
UART_Rx();
Timer_T0_sub(T0_delay_40us);

UART_Tx(0x55);	//Setup repeat operation
UART_Tx(setup_repeat_op);
UART_Tx(block_SZ);
Timer_T0_sub(T0_delay_40us);

UART_Tx(0x55);	//Send data
UART_Tx(ST | inc_byte_ptr);
for(int m = 0; m <= block_SZ; m++)
{
if(!(High_byte)){UART_Tx((*cmd_buffer) >> 8);High_byte = 1;}
else{UART_Tx(*cmd_buffer);cmd_buffer++;
High_byte = 0; prog_counter += 1;
}
UART_Rx();
Timer_T0_sub(T0_delay_40us);}

Fuse bytes
Quote: “Note: When writing the fuses write all reserved bits to ‘1’.” See section 6.10

There are fuse bytes for
WDTCFG	watch dog timer
BODCFG	BOD
OSCCFG	clock
SYSCFG0	system settings
SYSCFG1	SUT
APPEND	flash partition
BOOTEND	flash partition
Lock bit

WDTCFG	Leave as default	WDT under program control

BODCFG	leave as default	BOD disabled

OSCCFG	leave as default	Chip runs at 20MHz with internal clock

SYSCFG0	Write as 0xF7: No CRC, reset pin is UPDI, Eeprom preserved at chip erase
note bits 1, 4 and 5 are reserved.

SYSCFG1	Leave as default (7): 64mS SUT. Write to 5: 16ms SUT (to test fuse writing subroutine)

APPEND
BOOTEND	Leave both as default: No flash partitions set up.

Lock bit	Write 0xC5 to leave the device open; zero to lock it.	Always reads as zero.