UNO_as_UPDI_programmer: Development notes for ATtiny806/16/6
(Unified program and debug interface)

Step 1: Programmer takes control of the reset line. See data sheet 6.10.4.4

Operation of the reset line is determined by the fuse SYSCFG0 bits 3 and 2.
Factory default sets these bits to 0x1
This means that the reset pin connects to the UPDI programmer every time that a reset occurs.

UPDI initialisation	see 30.3.2.1

Programmer action	UPDI action
Issue reset	Detects reset and converts reset line to WPU
Detects the WPU / Drives line low for TDeb0 / (1uS max)	Detects the low ad holds it low for TUPDI (200us max) and then starts a timer TDebZ (1400uS max)
Waits for line to go high
Sends SYCH pulse	Receives SYNCH pulse or times out and restores reset function.

Note During operation of a user program a period of less that 2mS will be added to the start-up time following a reset.

Programmer operation
UNO clock is 16MHz. A 16 x nop takes 1uS
Issue reset
Wait 0.25uS
Drive reset low
Wait 0.75uS
Poll the line until it goes high
Wait 2uS
Send SYNCH