UNO_as_UPDI_programmer: Development notes for ATtiny806/16/6
(Unified program and debug interface)

Step 1: Programmer takes control of the reset line. See data sheet 6.10.4.4

Operation of the reset line is determined by the fuse SYSCFG0 bits 3 and 2.
Factory default sets these bits to 0x1
This means that the reset pin connects to the UPDI programmer every time that a reset occurs.

UPDI initialisation	see 30.3.2.1

Programmer action	UPDI action
Issue reset pulse	Detects reset and converts reset line to WPU
Detects the WPU / Drives line low for TDeb0 / (1uS max)	Detects the low and holds it low for TUPDI (200us max) and then starts a timer TDebZ (1400uS max)
Waits for line to go high
Sends SYCH pulse	Receives SYNCH pulse or times out and restores reset function.

Note During operation of a user program a period of less that 2mS will be added to the start-up time following a reset.

Programmer operation
UNO clock is 16MHz. A 16 x nop takes 1uS
Issue reset pulse
Wait 0.25uS
Drive reset low
Wait 0.75uS
Poll the line until it goes high
Wait 2uS
Send SYNCH

Note: Reset lines are normally connected to a 10K pull up resistor. Hence the 0.25uS delay rather than polling to determine presence of the UPDI connection.

Programmer UART operation	see 30.3.1

The UART clocks data out of the Tx shift register bit zero first and
clocks it through the Rx shift register entering at bit seven.

The SW UART implemented in the UNO does not use a shift register. However it both transmits and receives bit zero first. The clock will initially be set by a 1ms delay so that SW latency can be ignored. Once data flow is working properly the clock will be speeded up as much as possible.

In the final implementation clock delay will take the form
for(int m…...){asm("nop");}
and be slightly different for receive and transmit functions.
UART Transmission
The UART clocks a data byte out starting with bit 0.

Parity = 0;
For (int n……..){
If (data_byte_T & (1 << n))
{out_h; parity += 1;} else out_l;clock_delay_T;}	//clock data out
if (parity%2)out_h; else out_l;clock_delay_T;	//clock parity bit
out_h;	//initiate stop bit

UART Reception
The UART clocks a data byte in starting with bit 0.

Wait for start bit
clock_delay_R/2;
For (int n……..){
If (input_h){data_byte_R |= (1 << n);
clock_delay_R;}

data_byte_R will be interrogated on a pc and clock_delay_T adjusted with clock_delay_R to achieve synchronisation between Rx and Tx.

Terminating a UPDI session	see 30.3.2.3

Reading the signature bytes

The programmer sends the LDS command and then waits for a start bit heralding a response from the UPDI.
The command is
0 0 0 0 0 0 0 0	where
bits 0 and 1 indicate a data size of 1 byte
bits 2 and 3 indicated an address size of 1 bytes
bit 4 in unused
bites 5-7 indicated the LDS command

The address is then sent immediately.
The addresses of the signature bytes are 0, 1 and 2	see 6.7

The entire command string is
Tx_byte 0x55	Synch command
Tx_byte 0	LDS command
Tx_byte 0	Data address
Wait for response.	Data

Repeat for addresses 1 and 2 for all 3 signature bytes
Continue reading for addresses beyond 3. They may contain serial numbers, cal data plus fuses. Not sure.

Reading the fuse bytes
The CPU reads fuses starting from a base address of 0x1280. If they were not found with the signature bytes repeat the procedure just given given above but use this address.

Development setup:

Develop the code in Atmel studio.
Copy it into an Arduino sketch
Upload it to a UNO.
Connect the target device to the UNO and run the code.