UNO as UPDI programmer

NVM/UPDI commands

UART_Tx (download_SIB)	Data sheet 30.3.3.8
Download_SIB is defined as E5
E5 is a key instruction download 128 bytes of SIB data

In subroutine	Erase_code()

send_key(Key_chip_erase);	Initiates a device erase command

UART_Tx(LCDS | ASI_KEY_STATUS_reg);
Downloads the UPDI key status register
If bit 3 is 1 the chip erase command was successful
UPDI reset
UART_Tx(STCS | ASI_Reset_Request_reg);
UART_Tx(Reset_signature);
Sends the reset signature 0x59 to the UPDI register
Sending zero releases the rest

UART_Tx(LCDS | ASI_SYS_STATUS_reg);
Downloads the UPDI key status register
If bit zero is 0 the device is unlocked

In subroutine	set_up_NVM_prog()

send_key(Key_NVM_prog);	Initiates NVM programming

UART_Tx(LCDS | ASI_KEY_STATUS_reg);
Downloads the UPDI key status register
If bit 4 is one NVM programming key is active

UART_Tx(LCDS | ASI_SYS_STATUS_reg);
Downloads the UPDI system status register
If bit 3 is one NVM programming can start

In subroutine read_out_signature_bytes()

UART_Tx(LDS_from | word_address);
Downloads data
Must be followed by address of data

Programming flash using isolated STS commands

UART_Tx(STS | word_address);
Followed by address
Then waits for AK byte
Then sends data byte

Subroutine Write_page_to_NVM()

UART_Tx(STS | int_data);	Store integer data command
UART_Tx(NVMCTRL_ADDR_reg);	Followed by destination address
UART_Tx(NVMCTRL_ADDR_reg >> 8);	Low and high bytes
Receive Ack Pulse
UART_Tx(PA);	Page address low and high
UART_Tx(PA >> 8);	bytes to be stored
Receive Ack pulse

UART_Tx(STS | byte_data);	Store data byte command
UART_Tx(NVMCTRL_CTRLA);	Followed by destination
UART_Tx(NVMCTRL_CTRLA >> 8);	address. High & low bytes
Receive Ack pulse
UART_Tx(WP_cmd);	Send write page command
 Receive Ack pulse

Subroutine write_fuse()
For this subroutine it was found that UART_Tx(STS | int_data) would not work properly. It onlr save the lower 8 bits.
UART_Tx(STS | int_data) was therefore replace by:
UART_Tx(STS | byte_data)
UART_Tx(STS | byte_data)
as follows:

UART_Tx(STS | byte_data);	Store data byte command
UART_Tx(NVMCTRL_ADDR_reg);	Followed by destination address
UART_Tx(NVMCTRL_ADDR_reg >> 8);
Receive Ack pulse
UART_Tx(fuse_add);	Address of fuse low byte
Receive Ack pulse

UART_Tx(STS | byte_data);	Store data byte command
UART_Tx(NVMCTRL_ADDR_reg);	Followed by destination address
UART_Tx(NVMCTRL_ADDR_reg >> 8);
Receive Ack pulse
UART_Tx(fuse_add >> 8);	Address of fuse high byte
Receive Ack pulse

UART_Tx(STS | byte_data);	Store data byte command
UART_Tx(NVMCTRL_DATA_reg);	Follow by address
UART_Tx(NVMCTRL_DATA_reg >> 8);
Receive Ack pulse
UART_Tx(value);	New fuse setting
Receive Ack pulse

UART_Tx(STS | byte_data);
UART_Tx(NVMCTRL_CTRLA);
UART_Tx(NVMCTRL_CTRLA >> 8);
Receive Ack pulse
UART_Tx(cmd_update_fuse);	Send the command to update the fuse
Receive Ack pulse
Block data write to flash	(using repeat command)

waitforkeypress();
newline();
UART_Tx(0x55);
UART_Tx(ST | pointer);	//Use ST to store 2 byte pointer
UART_Tx(Add_in_flash);
UART_Tx(Add_in_flash >> 8);	//Address to be stored in pointer register
UART_Rx();	//Ack pulse
Timer_T0_sub(T0_delay_200us);

UART_Tx(0x55);
UART_Tx(ST | inc_word_ptr);	//Store byte & increment pointer
UART_Tx(flash_data_byte >> 8)
UART_Tx(flash_data_byte)
Timer_T0_sub(T0_delay_200us);

UART_Tx(0x55);
UART_Tx(setup_repeat_op);	//Setup repeat operation
UART_Tx(0x3F);	//Repeat until page buffer is full
UART_Tx(0x55);
UART_Tx(ST | inc_ptr);	// Store byte & increment pointer
for(int m = 1; m <= 0x3F; m++){
  UART_Tx(flash_data_byte)}

for(int m = 0; m <= 55; m += 2){
  sendHex(16, ((array[m] << 8) | array[m+1]));
  Timer_T0_sub(T0_delay_5ms);}